## Slide 1: ECE M216A project UCLA
Design Features
Used only 10 multipliers and 10 adders. Less area and minimum number of blocks design.
Combined with pipelining and parallelism design. Each neuron has only 1 multiplier and 1 adder with pipelining process. 10 neurons with parallelism structure.
Feedback loop design allows one adder to add up all values.
Object oriented design. Put max_selector and neuron as the sub-module and use them in Image_Classifier which is the top module
M
A
R
R

## Slide 2: Synthesis Result
Technology | Synopsys 32nm
Core Area | Total cell area: 0.54093 mm^2 Total area: 0.929131 mm^2
Power | Internal power: 4.1787 mW Switching power: 0.6171 mW Leakage Power: 0.9 W Total Power: 0.90516 W
Energy/Image | Ptotal*Nclk*Tclk= 1.477 uJ/Image
Energy-Area Product | 1.372 uJ*mm^2
Clock Period | 2ns
N clk Cycles to finish | 816
Delay | 1632ns

## Slide 3: Accuracy result
89% for 200 images
84% for 500 images
98% for 1000 images